## Slide 1: Status of the Mars Entry Atmospheric Data System (MEADS) Hardware and Flight Data Reconstruction Effort Presentation at IPPW-9 20 June, 2012 Toulouse, France
Michelle M. Munk
NASA-Langley Research Center

## Slide 2: Acknowledgements
Team Members (and coauthors, in bold) contributing to the MEADS flight data reconstruction effort:
  Mark Schoenenberger (Lead)
  Chris Karlgaard (simulation)
  Prasad Kutty (simulation)
  John Van Norman (aerodynamics)
  Jeremy Shidner (trajectory)
  Noah Favareh (aero testing)
  Robert Blanchard
  Rafael Lugo (Aberdeen testing, Monte Carlo methods)
  Robert Tolson
  Sean Commo
  Scott Striepe
  Chris Kuhl (MEDLI Chief Engineer)
  Alan Little (MEDLI PM)

## Slide 3: MEDLI System Objectives
Aerodynamics & Atmospheric
  Confirm aero at high angles of attack
  Separate aerodynamics from atmosphere
  Determine density profile over large horizontal distance
  Determine wind component
Aerothermal & TPS
  Verify transition to turbulence
  Determine turbulent heating levels
  Determine recession rates and subsurface material response of an ablative heatshield at Mars conditions

## Slide 4
On Our Way to Mars!
SSE Box
STI Transducer
Mars Science Laboratory
Heatshield
MEADS Port
Launch – 26 Nov 2011

## Slide 5: MEADS Pressure Data (In-Flight Zero)
MEDLI Cruise Checkout in March
All sensors functioning
  Average MEADS Transducer Temperature = -65°C
  Thermally stable SSE Temperature = +35°C
MEAD S/N | Calibration Model (from thermal vac) (mV) | In-Flight Zero (mV) | Difference
022 | -0.37 | -0.27 | 0.1
025 | -0.48 | -0.39 | 0.09
029 | -0.75 | -0.70 | 0.05
021 | -0.52 | -0.39 | 0.13
032 | -0.15 | -0.08 | 0.07
023 | -0.70 | -0.70 | 0.0
024 | -0.90 | -0.81 | 0.09
Note: In-flight zero data will be used to update the calibration model prior to entry
Cruise Checkout

## Slide 6: MSL EDL Timeline
Entry
E+240 s
E+81 s
E+91 s
E-0 s
E+226 s
Peak Heating
Peak Decel.
Deploy Parachute
SUFR
EBMD Jettison
h: ~125 km
V: ~5.8 km/s
q > 850 Pa
h: ~26 km
V: ~4.6 km/s
h: ~19 km
V: ~3.7 km/s
h: ~12 km
V: ~0.53 km/s
h: ~10 km
V: ~0.47 km/s
INTERFACE
Mach
3.3
Mach
28
MSL Entry Vehicle
4.5 m diameter
70 deg sphere-cone
Entry Mass: 3200 kg
Hypersonic L/D: 0.24
Trim AoA: 17 – 20 deg
Mach
2.1
MEDLI
data off
MEDLI
data on
E – 10 min

## Slide 7: MEADS Science Objectives
Level 2 Requirement | Objective | Accuracy
PS-371 | Reconstruct basic surface pressure | None specified
PS-372 | Reconstruct Angle of Attack | ± 0.5˚ when P > 1750 Pa
PS-373 | Reconstruct Angle of Sideslip | ± 0.5˚ when P > 1250 Pa
PS-374 | Reconstruct dynamic pressure | ± 2% when P > 850 Pa

## Slide 8: MEADS: Angle of Attack Uncertainty*
MEADS angle-of-attack requirement
Requirement not met at low supersonic conditions
Low q: Low signal-to-noise
Curves end at
850 Pa limits
*Perfect CFD assumed

## Slide 9: MEADS: Angle of Attack Uncertainty
MEADS alpha requirement
Curves end at
850 Pa limits

## Slide 10: CFD Uncertainty and Calibration
CFD V&V Test Facilities:
LaRC UPWT
  Mach 2.5, 3.5, 4.5 Pressure model
  Flow Angularity survey
LaRC 31” Mach 10
  Pressure model
UPWT Flow Angularity
November, 2011
Mach 10 Pressure Test
November, 2011

## Slide 11: Aberdeen Proving Grounds Ballistic Range Test
A series of ballistic range tests were conducted to demonstrate and refine the reconstruction approaches.
Each model telemetered onboard pressure, accelerometer, rate and magnetometer data, and tracked by radar.
Testing in air makes wind tunnel data directly relevant (no CO2 vs Air uncertainty)
RADAR tracking provides inertial trajectory path “truth” to within meters.
MET data provides Mach measurements with accuracy of RADAR velocity measurements.
Aberdeen Proving Grounds 7” Gun
Initial Mach: ~3.6
~10 kHz data rate
~10 s flight data
Example CEV pressure data (Aug 2009)
6.75” diameter
16.2 lb
Kulite transducers read MEADS pressures
IMU telemetry package

## Slide 12: Reconstruction Tool Testing
Comparing 3 independent reconstructions with uncertainties identifies suspect data
In addition to MEADS,
uncertainty analysis of all data sources is being done concurrently
We are HERE,
working with simulated
data from MSL team
Using MSL design trajectories with simulated telemetry, run all 3 methods and compare results

## Slide 13: Reconstruction Tool Test: Dynamic Pressure (3s low CA case)
Inertial reconstruction slightly high
ADB reconstruction slightly low
MEADS pressure readings tell us that everything is fine; it’s an aero database problem
MEADS data improves observability of the issues

## Slide 14: Additional Reconstruction Work
POST-based reconstruction (Striepe and MSL trajectory team)
  Extended Kalman filter in POST2 architecture
  Utilizes MSL flight simulation (best state estimates available for EKF)
  This effort will become an updated version of the MSL trajectory team’s reconstruction work done for past Mars Missions.
Reconstruction NRA awarded to NIA university team (Robert Blanchard, PI)
  Adds statistical uncertainty analysis to existing reconstruction methods
  This effort will add continuity to the independent reconstructions funded by recent Mars missions. New capabilities (and new data) should improve (and better quantify) accuracy.
MISP Reconstruction relies somewhat upon reconstruction of MEADS data
The combined comparison of all of these reconstructions (each with the benefit of the MEADS data) will provide the best assessment of the MSL trajectory, help understand data from past missions, and yield the most information to assist future missions.

## Slide 15: Current Status of MEDLI Project
2 Cruise checkouts have occurred (March, April 2012)
  Full dataset returned for practice with formatting, check against qualification testing ranges, etc.
Working with JPL and EDL simulation team to determine data flow, products, and timing (first team meeting was 12/14/11)
All primary MEADS reconstruction codes for processing flight data have been written and checked out
Held Peer Review of methods in January 2012
Reconstruction Readiness Review in late July at ARC
Entry: August 6, 2012 ~1 a.m. EDT
  MEDLI Operations Engineer, Chief Engineer, MEADS Reconstruction Lead will be at JPL for entry
  “Real-time” data: 16 selected measurements at 1 Hz
  MEDLI also generates tones during EDL: 5 catastrophic, 3 progressive
  Anticipate full dataset 1-2 weeks after landing

## Slide 16: MSL/MEDLI Reconstruction Process
Doc
Rev B
+ JSR Special Issue
1RTDP
integrated from
top down.
2Needs full data set
plus HiRISE
Image.
3JPL GN&C subsystem is on contract to do this.
L + 1-2
days
L + 1-2
weeks
~ 3
months
~ 4
months
1
year
Level ≤ 3
Configuration-controlled,
Filtered Data Drop
Level 4
Level 4+
Heat Shield Rot., Defl., Translation
MEADS Data
Other Sources
(Radiometric)
MCS
Mesoscale Model
Kalman Filter
Adjudication
Resolve Discrepancies&
Write Papers
MISP Initial Product MISP-II MISP-III
~ 2 times/week meetings
Issues/
Discrepancies
List
L + 2 wks
BET
Doc
Rev A
PET1
PBET2,3
Flight
Data
Level 0

## Slide 17: Thank you!

## Slide 18: Backup

## Slide 19: Motivation and Benefits of Aeroballistic Testing
Flight data from aeroballistic testing can be used to test various reconstruction techniques (data sources include IMU, pressure taps, and radar)
Radar tracking data permits comparison to “truth” trajectory solution (inertial position and velocity)
Other available data: magnetic field vector from magnetometers and MET data
Deliverables

## Slide 20: 1σ Uncertainty Stackup Example: P1
20
Dashed lines show ± 1% bound on averaged experimental data.