## Slide 1: A simple, robust and adaptable strategy for ballistic landings on small binary bodies.

## Slide 2: An increased interest for binary asteroids
Discovery mission proposal BASiX
ESA Cosmic Vision Marco Polo R.
P.I. Dr Daniel Scheeres
P.I. Dr A. Barucci & Dr P. Michel
We need robust ways for delivering unpowered landers to the surface of asteroids, while ensuring the safety of the mothership.

## Slide 3: Summary of the Presentation
System Description
Feasibility of Strategy
Landing From L2
Grounding the Lander
Strategy Design
Jacobi integral
e.g. 1999 KW4
0-Velocity surfaces
Periapses maps
R.T.O.
Manifold deliveries
Release margins
Conley criterion
Linearizing
System Description

## Slide 4: The exemple: 1999 KW4
Binary asteroid system:
  Alpha (1.5km)
  Beta (500m prolate) tidally-locked with Alpha
  Mutual orbit parameters:
    a = 2.5km
    e = 0
Extensively studied
Representative of binaries (and very similar to 1996 FG3)
System Description

## Slide 5: Zero-Velocity Surfaces
The ZVS separate accessible and forbidden zone of state space
System Description

## Slide 6: A typical trajectory bundle
Strategy Design
L1
L2
Landing Zone
Outline of the 0VS
Trajectories from L2
Zone of Lander Deployment
ALPHA 1.1 mile
Landing Only
Beta

## Slide 7: Our landing strategy
Phase 1: L2 Approach
Phase 2: Ballistic Trajectory
Phase 3: Bounces
Strategy Design
ALPHA 1.1 mile

## Slide 8: Introducing periapses Poincaré maps
Feasibility
An acceptable landing trajectory is defined as
a trajectory whose 1st periapsis lies under the asteroid surface.

## Slide 9: The shape of the first periapsis region
The 1st periapsis region grows with energy
Feasibility

## Slide 10
Problem has too many variables:
  Mass fraction µ
  Energy C
  Shape and size of the asteroid
RTO : Radius-To-Orbit ratio is the radius in normalized units (e.g. , 6.9% for 1999 KW4)
Manifold delivery reduces to two variables: µ and RTO.
  If 1st periapsis<RTO then OK for some range of C
  If 1st periapsis>RTO then dangerous for any range of C
Manifold deliveries and RTO
Feasibility

## Slide 11: Feasibility of the strategy
Feasibility
Landing on the primary (Alpha)
Landing on the secondary (Beta)
If your secondary fits above this line, the strategy works!

## Slide 12: Aiming at the asteroid
All trajectories that enter the secondary’s region will impact…
… how can we ensure that our lander will enter this region ?
Following Conley (1968), linearizing at L2, we obtain a criterion on the polar angle of velocity at the neck.
Landing from L2

## Slide 13: A representation of Conley’s criterion
Landing from L2

## Slide 14: Matching analytics with simulations
60m
180°
Landing from L2

## Slide 15: Grounding the lander
We reach the surface… but do we land ?
Neck closure criterion
7% speed damping at impact is sufficient
Grounding Lander

## Slide 16: Main features of the landing strategy
Landing on the secondary is feasible for the vast majority of binary NEOs.
The deployment consists in releasing the lander in the L2 neck with a designated velocity direction and speed.
No GNC needed for the lander.
No risk for the mothership.
Margins that applies on deployment conditions are (for KW4) :
  -100m to +100m on the nominal y-axis release position
  0% to 500% error the nominal deployment speed
  -90° to +90° on the nominal velocity direction

## Slide 17: Questions?
L1
L2
Landing Zone
Outline of the 0VS
Trajectories from L2
Zone of Lander Deployment
ALPHA 1.1 mile
Landing Only
Beta